| 1. Department / Location WOODLARKS CAMP SITE | 2. Activity Area Aerial Runway | 3. Risk Assessor NICK RICHARDS/ SARAH LANE Date of Initial Risk Assessment 2nd March 2020 Signature | 4. No of Persons at Risk ONE PLUS | 5. Assessment Serial No 013 |
| --- | --- | --- | --- | --- |
| 6. Significant Hazard | 7. Risks | 8. Current Control Measures | 9. Initial | 10. Further Action Required. If yes state action. Controls / Procedures / Authorisation Training / Modification to Equipment or Process | 11. Revised |
|  |  |  | P | S | RR |  | P | S | RR |
| Using Aerial Runway | Rider Falling from aerial runway Falling if metal platform is opened too soon Falling from platform into valley Being hit by chair on far side of valley Chair descending too quickly into the landing area | Driver and ride supervisors must read the Aerial Runway book and safety section, be familiar with its working and be able to react in an emergency Max wt of rider 150kg No doubling up of riders with helpers Rider must sit still in chair and have safety straps in place. Clear platform of helpers before gate is removed for riders descent and place chain over entrance before ride commences Ride supervisors and bystanders to stand back behind the white box. Chair to descend at low speed into landing bay. There must be adequate ride supervisors – depending on the needs of each camper. | 2 1 2 2 | 4 4 4 3 | 8 4 8 6 | Individual risk assessments for rider as necessary. To seek the advice of the warden on it’s operation if they are a new user. | 1 1 | 4 3 | 4 3 |
| 12. Risk Rating PROBABILITY SEVERITY OF INJURY 1 Most Unlikely 1 Trivial injury/ies 2 Unlikely 2 Slight injury/ies 3 Likely 3 Serious injury/ies 4 Most Likely 4 Major injury/ies or death Multiply Probability (P) by Severity (S) to give Risk Rating (RR) | 13. Risk Rating RATING BANDS ACTION REQUIRED 1&2 Minimal Risk Maintain control measures. 3&4 Low Risk Review control measures. 6&8 Medium Risk Improve control measures. 9,12,16 High Risk Improve controls immediately & consider stopping work. | 14. Line Manager’s Final Certificate (Person responsible for Activity /Process) I certify that a suitable and sufficient assessment of the risks associated with the Activity/Area at 1/2 above has been carried out by a competent person and that the residual risks have been reduced to the lowest level reasonably practicable. Name Signature Date ………………. First Review |
| 15. Line Managers Review 1 2 3 4 |  |
| Name |  |  |  |  |  |
| Position |  |  |  |  |  |
| Signature |  |  |  |  |  |
| Date |  |  |  |  |  |