| 1. Department / Location WOODLARKS CAMP SITE | 2. Activity Area Kitchen Equipment Safety | 3. Risk Assessor NICK RICHARDS/ SARAH LANE Date of Initial Risk Assessment 2nd March 2020 Signature | 4. No of Persons at Risk ONE PLUS | 5. Assessment Serial No 014 |
| --- | --- | --- | --- | --- |
| 6. Significant Hazard | 7. Risks | 8. Current Control Measures | 9. Initial | 10. Further Action Required. If yes state action. Controls / Procedures / Authorisation Training / Modification to Equipment or Process | 11. Revised |
|  |  |  | P | S | RR |  | P | S | RR |
| Injury from Kitchen Equipment Musculoskeletal injury, cuts, grazes digit mutilation. | All Kitchen electrical equipment Potato Peeler Food Processer, Food Mixer Stick Blender, Jug Blender Electric Knife Microwave Cooker Sharps | Only to be used by trained Cooks authorised by Camp Leader. Before use, visual check to ensure no damage to electric cable. switch off electric supply after use, for removal of contents and cleaning. Competent operator, stand on a firm surface, area clear of people and cable kept clear of blade. Keep hands clear of blades at all times. All items to operated on firm surface in accordance with manufacturers guidance, see above All sharps, knives to be kept in safe container when not in use. Ensure responsible use of knives at all times | 2 1 2 1 | 3 4 3 3 | 6 4 6 3 | All Electrical equipment is subject to Annual PAT Any item found to be defective should be isolated, removed from service and reported to the Warden No loose clothing likely to be caught in mechanism Sign by the machine stating ‘do not put hands inside whilst machine is in motion’ Microwave :No metal containers or foil or be used Do not operate empty Beware of Operation when pacemaker wearers are in vicinity Do not place sharps and knives in washing up water when unattended | 1 1 1 1 1 1 | 2 2 3 2 3 2 | 2 2 3 2 3 2 |
| 12. Risk Rating PROBABILITY SEVERITY OF INJURY 1 Most Unlikely 1 Trivial injury/ies 2 Unlikely 2 Slight injury/ies 3 Likely 3 Serious injury/ies 4 Most Likely 4 Major injury/ies or death Multiply Probability (P) by Severity (S) to give Risk Rating (RR) | 13. Risk Rating RATING BANDS ACTION REQUIRED 1&2 Minimal Risk Maintain control measures. 3&4 Low Risk Review control measures. 6&8 Medium Risk Improve control measures. 9,12,16 High Risk Improve controls immediately & consider stopping work. | 14. Line Manager’s Final Certificate (Person responsible for Activity /Process) I certify that a suitable and sufficient assessment of the risks associated with the Activity/Area at 1/2 above has been carried out by a competent person and that the residual risks have been reduced to the lowest level reasonably practicable. Name Signature Date ………………. First Review |
| 15. Line Managers Review 1 2 3 4 |  |
| Name |  |  |  |  |  |
| Position |  |  |  |  |  |
| Signature |  |  |  |  |  |
| Date |  |  |  |  |  |