| 1. Department / Location WOODLARKS CAMP SITE | 2. Activity Area Aerial Runway | 3. Risk Assessor Lynne Cooper Date of Initial Risk Assessment 03/03/2024 Signature | 4. No of Persons at Risk ONE PLUS | 5. Assessment Serial No 013 |
| --- | --- | --- | --- | --- |
| 6. Significant Hazard | 7. Risks | 8. Current Control Measures | 9. Initial | 10. Further Action Required. If yes state action. Controls / Procedures / Authorisation Training / Modification to Equipment or Process | 11. Revised |
|  |  |  | P | S | RR |  | P | S | RR |
| Using Aerial Runway | Rider Falling from aerial runway. - Injury Falling if metal platform is opened too soon. - Injury Being hit by chair on far side of valley. - Injury Chair descending too quickly into the landing area. - Injury to rider | An Aerial Runway Handbook is in place for the safe use of the runway. Driver and runway supervisors will be conversant with the Handbook. Max weight of rider is 150kg. No doubling up of riders with helpers. Rider must sit still in chair and have safety straps in place. Platform to be clear of helpers before gate is removed for riders descent. Chain placed over entrance before ride commences. Ride supervisors and bystanders to stand back from the landing area. Controller will ensure Chair descends at low speed into landing bay. Pre use checks of all equipment conducted prior to use. Person at landing platform to communicate with Operator as needed | 2 1 1 1 | 4 4 4 4 | 8 4 4 4 | Individual risk assessments for rider as necessary. Users to seek the advice of experienced operator on its operation if they are a new user. There must be adequate ride supervisors – depending on the needs of each camper. | 1 1 | 4 4 | 4 4 |
| 12. Risk Rating PROBABILITY SEVERITY OF INJURY 1 Most Unlikely 1 Trivial injury/ies 2 Unlikely 2 Slight injury/ies 3 Likely 3 Serious injury/ies 4 Most Likely 4 Major injury/ies or death Multiply Probability (P) by Severity (S) to give Risk Rating (RR) | 13. Risk Rating RATING BANDS ACTION REQUIRED 1&2 Minimal Risk Maintain control measures. 3&4 Low Risk Review control measures. 6&8 Medium Risk Improve control measures. 9,12,16 High Risk Improve controls immediately & consider stopping work. | 14. Line Manager’s Final Certificate (Person responsible for Activity /Process) I certify that a suitable and sufficient assessment of the risks associated with the Activity/Area at 1/2 above has been carried out by a competent person and that the residual risks have been reduced to the lowest level reasonably practicable. Name Signature Date First Review |